Bill of Materials

20”

35”

35”

35”

42”- 24”

28”

At every red mark on the picture above there will be connection joint where the outer diameter of the steel will slide over a small diameter of steel and will be connected using a t-handle locking quick-release pin attached to the frame by a lanyard.

7 – Blue 0.375” diameter, 2.5” long t-handle locking quick-release pins

7 – 3/64” diameter, 6” long 18-8 stainless steel loop-to-eye lanyards

6 – 0.375”-16, 2” long 303 stainless steel with rubber cushion swivel leveling mounts with threaded studs

Main 1.75” OD with 0.065” wall 4130 chrome moly cold drawn seamless

Inner 1.625” OD with 0.095” wall 4130 chrome moly cold drawn seamless

33.5’ of main diameter seamless tubing

4’ – 8’ of inner sleeved seamless tubing

1 – 60 x 3” heavy duty black cinch strap – 5 pack

1 – silent ball bearing 360° swing hanger

1 – platform swing

Padding for the frame